## Slide 1: Formal hardware verification: challenges and opportunities
Agile hardware center

## Slide 2: introduction
The need for better verification

## Slide 3: The verification challenge
Systems on a Chip (SoCs)
  Growing in size and complexity
  Single chip contains multiple cores, caches, accelerators
SoC Verification
  SoCs used in critical applications
  Correctness is essential
  Failures can be extremely costly (Intel FDIV: $500M)
  Verification dominates design

## Slide 4: Template layout options
All template layout options can be found using the “Insert” tab and choosing “New Slide” dropdown box in PPT.
Slide from DARPA CRAFT proposer’s day

## Slide 5: Formal Verification
Has potential to revolutionize verification
  Better than testing: covers all possible cases
  Already used extensively in industry
  But there are many challenges
Three main steps
  Create a mathematical model of the system
  Specify formally what the properties of the system should be
  Prove that the model has the desired properties

## Slide 6: Formal Verification
Model
Specification
Verifier
Proof
Or
Bug Trace

## Slide 7: modeling

## Slide 8: modeling
Good news: HDL descriptions are already a formal model
Challenges
  Lack of non-commercial tools that can parse modern HDL’s
  Analog / mixed-signal components
  Closed-source IP can’t be modeled precisely
Solutions
  New open-source toolchains are being developed
  AMS circuits can often be approximated by digital circuits
  New initiatives to build open-source hardware

## Slide 9: Open-source Formal verification Flow
Yosys: open-source front-end for Verilog
  Optional (commercial) Verific front-end for full SystemVerilog support
CoreIR: “LLVM for hardware” open intermediate representation
CoSA (CoreIR Symbolic Analyzer): open source formal analysis (model checking, bounded model checking)
CVC4: open-source SMT solver
CoSA
Yosys
(Verilog)
CoreIR
Verific
(System-
Verilog)
Open Source
CVC4
(SMT Solver)

## Slide 10: specification

## Slide 11: Specification
Challenges for today’s techniques (e.g. assertion-based verification)
  Requires design knowledge
  Requires manual effort
  If incomplete, then will miss bugs
Solutions
  Integrated verification and design
  Symbolic QED – no manual specification needed
    Technique developed together with Prof. Subhasish Mitra

## Slide 12: Integrated verification: Equivalence checking
Comparison of a CoreIR design before and after optimization pass
CoreIR optimization pass provides information about constants folded directly to CoSA
Significant performance improvement: 1.3 min vs. timeout (2 h)
Design
Design’ (after pass)
Equivalence Proof
Counterexample
Constants Folded
Equivalence Property
TS1 x TS2
Candidate Lemmas
Equivalence Check via SMT Solving
CoSA
Encoders

## Slide 13: quick error detection
Quick Error Detection (QED)
  Technique developed by Subhasish Mitra’s group
  Uses shadow registers and memory
  Applies duplicate and check transformation to improve tests
 | Regular | Shadow
Registers | R0-R15 | R16-R31
Memory | 0x10000-0x1FFFF | 0x20000-0x2FFFF
…
LD R1, [0x10000]
LD R2, [0x10040]
…
LD R1, [0x10000]
LD R2, [0x10040]
LD R17, [0x20000]
LD R18, [0x20040]
CMP R1 == R17
CMP R2 == R18

## Slide 14: Symbolic quick error detection
Combines formal methods with QED
  Leverages idea of self-consistency (Jones ‘96)
  Does there exist any sequence of instructions that would fail a QED test
  Searches all possible sequences using bounded model checking
  Runs automatically overnight
Some results
  OpenSPARC T2: found 92/92 tough bugs automatically
    Few minutes to few hours each
    Each found bug returned a bug trace of less than 10 instructions
  RIDECORE: (open-source out-of-order Risc-V core)
    Found previously unknown bug
    Bug was reported and fixed

## Slide 15: Symbolic quick error detection
Surprisingly, can be made into a complete technique
  SQED can, in theory, find all bugs in a processor core
  Limited only by the power of the bounded model checker
Can be extended beyond processor cores
  Same idea can be used for accelerators
  Instruction-level abstraction (ILA) developed by Malik and Gupta at Princeton makes accelerators look like processors
Techniques for scaling up (work in progress)
  Symbolic initial states
  Automatic design partitioning
  Abstraction of uninteresting components

## Slide 16: proving

## Slide 17: Proving
Challenges
  Manual proofs require enormous effort
  Automated techniques limited to small designs
Solution:
  Better Solvers!

## Slide 18: Evolution of SMt solving
Comparison of virtual best SMT solvers since 2010
Evaluation on 39610 benchmarks (SMT-LIB 2018)
41 different families of benchmarks
Quantifier-Free Bitvector (QF_BV) SMT-LIB benchmarks

## Slide 19: Evolution of smt solving
Chart: 
| 2010 | 2011 | 2012 | 2014 | 2015 | 2016 | 2017
 | 4314707.24 | 1534283.12 | 672319.5 | 553594.48 | 517087.09 | 481784.13 | 389777.21
Total time (virtual best)
Average speedup: 11X
Unsolved (2010): 3100
  All but 200 solved now
  Over 2000 now solved in less than 1 second

## Slide 20: How will we get even better solvers?
Leverage SAT technology
  SAT solvers also improving each year
Build better SMT solvers
  More powerful rewriting and algebraic reasoning
  New SMT theories
  Specific optimizations for bounded model checking
  Parallel computing
  Machine learning

## Slide 22: Agile hardware flow
Halide
Place and Route
Yosys (Verilog)
…
CoreIR
High-level Functional Definition
Intermediate Circuit Representation
Bitstream CGRA configuration
Improve hardware design productivity with ideas from software
Start with a high-level description language for image processing, e.g., Halide
Uses CoreIR as a representation throughout the flow
Allows for multiple front-ends such as Yosys
Inspire design re-use and innovation by providing open-source toolchain

## Slide 23
Model and Properties as single entry point to the model-checker
Bitblasting loses word-level structure
Black-box usage of SAT solver
Closed source
System Model
Properties
Model Checker
SAT Solver
BMC and k-induction engines
Leverages CoreIR circuit representation developed as part of Stanford agile hardware (AHA) project
Can make use of additional design information to optimize verification
Maintains word-level structure by using SMT theories
Uses customizable SMT solver developed by Barrett group at Stanford
Entire toolchain is open-source
System Model
Design Information
SMT Solver
Properties
CoSA Model Checker
Model Checking (Commercial Tools)
CoreIR Symbolic Analyzer (CoSA)