## Slide 1: AHA (Agile Hardware): Progress & Plans
10/14/2018
Clark Barrett, Kayvon Fatahalian, Pat Hanrahan,
Mark Horowitz, Priyanka Raina

## Slide 2: Team
Pat Hanrahan Clark Barrett Kayvon Fatahalian Priyanka Raina

## Slide 3: The Semiconductor Business is Changing
Scaling is slowing
Chip design is very expensive
The industry is consolidating
Good VLSI designers are now all going to systems companies
  The industry is re-integrating

## Slide 4: Specialized Hardware - DSSoC
Tegra X1
Apple A9

## Slide 5: The New Challenge:
How to efficiently create these systems w/ accelerators
  Which is much harder than producing the accelerator
Porting an application to hardware
  Is about reframing the algorithm as much as hardware design
  Need expertise in the application area and hardware design

## Slide 6: AHA – Agile Hardware
It is partly a mindset, but it is more than that
Start with application
Quickly map to hardware
Repeat

## Slide 7: Success Depends On Avoiding:
Specialized Hardware Mistake
Save Computing Mistake

## Slide 8: The Specialized Hardware Mistake
Study the application
Build the hardware
Then write the software for the machine
  And that is the only application this hardware will ever support…
Repeat

## Slide 9: This Is The
Model of Design

## Slide 10: Doesn’t Address The Biggest Issue
Source: IBS
Notes: To move to the next slide: So how do we deal with complexity? How have we historically dealt with it?

## Slide 11: To Quickly Map App to Hardware
Need Some Isolation
Application
Architecture

## Slide 12: The Abstract Hardware Model
Accelerators only work for local, compute intensive, applications
  Everything else will be limited by the memory system
Our hardware IR should be good for these applications
(Avoiding the Save Computing Mistake)

## Slide 13: Optimizing with an “ISA” An Agile Approach to Accelerators
Key idea:
  Maintain end-to-end flow no matter what
  Always be able to compile new applications
Incrementally change tools/fabric to improve performance
Accelerator becomes optimization of underlying fabric
  Heterogeneous fabric, which may or may not need “new” instructions

## Slide 14: To Quickly Map App to Hardware
Application needs to be written in a DSL (Visual Computing)
  Halide
Compiler maps it to a programmable hardware model (ISA)
  CoreIR
Map, place/route lowered application to target hardware
  CGRA

## Slide 15: Why Halide
Separates schedule from function
Already is an embedded language
  Easy to indicate what should be accelerated
  Generates good code for the rest

## Slide 16: Why CoreIR
Formal semantics
  Facilitates formal checking of design flow
Representation (DAGs of operations)
  Matches the representation of our applications
Allows linking of inputs from other systems
  It isn’t ego-centric

## Slide 17: Why CGRA
It is universal
  It can map any application
It is a spatial architecture
  So we can make it look like any accelerator

## Slide 18: Also Need To Build The Hardware Target
This is an SoC with a CGRA
  Where the CGRA is continually being updated
  These updates improve the “accelerator”
Need to create a generator to create this SoC

## Slide 19: Progress and Plans
Application to coreIR
  Halide compiler work, autoscheduling
CoreIR, and mapping coreIR to CGRA
CGRA design, generating CGRA
Test and validation environment

## Slide 20: AHA Toolchain (working)
ASIC
Host code
CoreIR (LLVM for HW)
Fast simulation SMT-based verification
Optimization/Analysis Passes Technology/Mapping
Place and Route
Dataflow / Tensor
autoscheduler
Image processing DSLs: e.g., Halide, DNN IRs
Magma/Chisel
Gensis2
Verilog
Halide backend
FPGA
SMT
Checking
Stanford CGRA
Generator

## Slide 21: Halide to CoreIR
Newly implemented codegen capabilities
  ROM generation
  multi-dimensional linebuffers
  valid bit generation from linebuffers
Generating hardware from more applications
  Unit tests: logical right shift, counter, …
  Full apps: demosaic, optical flow, camera pipeline, …

## Slide 22: Halide to CoreIR Plans
Currently rebasing to top-of-tree
  First application complete: 3x3 convolution with updated compiler
Re-expressing scheduling primitives
  Hardware accelerator tiling based on GPU tiling
  Primitives for linebuffer and full pipeline throughput
Merge DNN and image hardware branches to top-of-tree

## Slide 23: Halide Auto-schedulers
Auto-schedulers
  Both for Halide and for Halide like IR (joint work with Google)
Complete scheduler for DNNs
  Can use any existing hardware

## Slide 24: Auto-scheduler Plans
Continue work on g.p. Halide scheduler
  Joint work with Andrew Adams, Facebook
Create auto-scheduler for joint hardware generation
  Streaming and blocking computations

## Slide 25: Addressing the Hard Problem:
No one wants hardware for this application
  They want hardware for this type of application
How to create the hardware they want?
  CGRA might be a solution
Look at creating generalize functions
  Explore different implementation options

## Slide 26: CoreIR to CGRA
Basic system is up and running
  Can read inputs from Verilog, FIRRTL, Rigel, Halide, Magma
Formal semantics
  Primitives have equivalent to SMT bit vectors
Created new P&R flow
  It is in use in current flow
Extensible framework
  Easy to add passes or extentions to the system

## Slide 27: Kernel Discovery from Dataflow Graph
Two convolutions
Two kernels
Cascade Example

## Slide 28: Placement Details
Force-Directed Global Placement
Simulated Annealing Detailed Placement

## Slide 29: CoreIR to CGRA Plans
Extend coreIR feature set to enable wider set of applications
  More operand types (e.g. floating point)
  More operators (div, generalized exponentials)
Extended coreIR and P&R analysis passes:
  Register retiming
  Improved mapping/packing pass for CGRA
Suggest changes to CGRA design to improve efficiency

## Slide 30: Taped Out Our First CGRA

## Slide 31: CGRA Plans
Fix problems with current system to make it easily buildable
  Create virtual tape-out flow
Increase capability of the FU
  Bfloat16 data types, divide, transcendental support
Memory hierarchies
  Fast reconfiguration, testing and debug support
Explore supporting dynamic launch, as used in modem processing

## Slide 32: Next-Gen CGRA Generator
See next talk

## Slide 33: Using Just-In-Time Compilation to Accelerate CGRA Simulations
Problem: Statically programmable datapaths are slow in conventional hardware simulators
Solution: just in time (JIT) compilation
Chart: Runtime (seconds)
| conv 2 x 1 | conv 3 x 1 | conv 3 x 3 | add snake | add/mem snake | harris
s1 | 75 | 120 | 326 | 556 | 568 | 2427
s2 | 84 | 121 | 324 | 613 | 658 | 1865
SJIT | 63 | 91 | 93 | 68 | 166 | 318

## Slide 34: CoSA: CoreIR Symbolic Analyzer
CoSA is an SMT-based symbolic model checker for hardware design
Open-source, and written in Python
Supports multiple input formats including: CoreIR, Verilog, and SystemVerilog
Provide state-of-the-art formal analyses, including: Linear Temporal Logic (LTL) and invariant verification, equivalence checking, proving capabilities, fault analysis, and more…
No
Yes
System Design
Expected Behavior
+
clk
en
out

## Slide 35: Testing and Validation
See last talk

## Slide 36: We Have a Complete System, But the Journey is Just Beginning
Thanks for helping with this project
It is great to be part of the next revolution in VLSI design