## Slide 1: Power Domains – IR Analysis

## Slide 2: Goals
ON Steady-state Power and IR Analysis
    Analyze how the insertion of power switches impacts power and IR drop when then the switches are in steady ON state
    Static or dynamic power can be used to do steady state analysis
  OFF Steady-state Power Analysis
    Analyze the total power saving and leakage when power switches are turned OFF
Power-up Analysis
    Analyze the time required to turn ON all the power gates
Rush Current Analysis
    Analyze the impact of rush current generated by the powering up logic on the AON power-grid voltage
Notes: .

## Slide 3: Steady State Analysis

## Slide 4: Steps Involved for Steady State Analysis
A. Read the physical design and SPEF file
    Read Innovus design which is the output of P&R
    Generate SPEF file from P&R
B. Power Grid Library Generation
    Used to create and modify a cell library database of PG views
    Creates a binary power-grid view of the cells and the technology libraries
    Collaterals needed: Technology LEF, cell LEF, Extraction file, Layer maps
Notes: .

## Slide 5: Steps Involved for Steady State Analysis
C. Power Gate Library Characterization
    Used to characterize the power switch’s on-resistance, leakage current when the power-gate is OFF and the saturation current
    This information is needed for IR drop analysis
    Collaterals needed: Technology LEF, cell LEF, Extraction file, Layer maps, SPICE netlist and SPICE device models
  D. Power Grid Information
    VDD/GND Net names
    VDD Supply Voltage
    VDD/GND Threshold
      Minimum allowed voltage on the power net or maximum rise on the ground net
      Threshold value is used to verify that the power grid passed the limit check
Notes: .

## Slide 6: Steps Involved for Steady State Analysis
E. Voltage Source Information
    Voltage source information can be specified by pad cells, power pins or by {X,Y} coordinates of the pad cells
  F. Power Data
    Provide power profile of the design
Notes: .

## Slide 7: Specifications
Parameter | Current Setup | Required Setup
Voltage | 0.72 V | 0.72 V
PVT | SS_0.72_-40C | TT?
Power Profile (for ON power analysis) | Default activities | ?
Power Profile (for OFF power analysis) | Default activities | ?
Voltage Source | Determined by power pins | Determined by bump locations
Notes: .

## Slide 8: Power Switch Analysis
Power gate transistor is modeled as a linear resistance
    Value is determined from the device model
  Impact of this resistance is modeled during static or dynamic power and rail analysis to ensure that sufficient switches are added in the design to satisfy the current requirement of the switched block
  Each switch is checked if it is operating in the non-saturated (linear resistance) region
  PASS: Switch is operating in linear resistance region
  FAIL: A switch is operating outside of the non-saturation region and drawing too much current
Notes: .

## Slide 9: Power Switch Analysis
Analysis at some high activity
Analysis at some low activity
Notes: .

## Slide 10: Power Switch Density Calculation
Operating Voltage =Vdd
Acceptable Voltage Drop (off-chip, package, on-chip etc) = ⍺Vdd
% of acceptable voltage drop on-chip (PG, switches etc.) = β(⍺Vdd)
Acceptable voltage drop across switches = ɣβ(⍺Vdd)
Power of the block (from P&R) = P mW
Current through block=P/Vdd mA
Acceptable resistance across the power switches = ɣβ(⍺Vdd*Vdd)/P Ω
Resistance of power switch = R Ω
No. of power switches = (R*P)/(ɣ β(⍺Vdd*Vdd))
Usually these values are ⍺=10%, β= 30%, assume ɣ= 50%,
So for Vdd=0.72 V, the acceptable drop comes to about 10.8 mV
Notes: .

## Slide 11: Power when tile is ON (Approx. power profile)
Notes: .

## Slide 12: Power after turning off the tile (Approx. power profile)
Notes: .

## Slide 13: PG IR voltage drop
Notes: .

## Slide 14: Instance based voltage drop
Notes: .

## Slide 15: AON IR drop when tile is OFF
Notes: .

## Slide 16: Functional Verification

## Slide 17: AON – SD Partitioning

## Slide 18: Layout

## Slide 19: IR Flow
  Determine if power switch count is sufficient
  Determine if power grid density is sufficient
  Check if IR drop on all cells is within threshold
  Review Memory vs PE PS/PG grid density requirement (Any special requirements for Mem?)

## Slide 20: PG Aware Power and Timing Analysis
  Wakeup time evaluation for the power switches
    Faster wakeup time good for timing, but high inrush current causing high IR drop
    Daisychaining good for inrush current – but need to verify the wakeup times
  Timing closure – No significant performance degradation
  Hold time analysis
  Review Memory vs PE Timing Analysis (Any special requirements for Mem?)
  Power saving evaluations

## Slide 21: Questions?