## Slide 1: CGRA Architecture and Design Methodology
Priyanka Raina
AHA Retreat
May 31, 2019

## Slide 2
MEM
MEM
MEM
MEM
PE
PE
PE
PE
PE
PE
PE
PE
MEM
MEM
MEM
MEM
Coarse Grained Reconfigurable Array (CGRA)
CGRA Programming
Toolchain
Halide Compiler
Application in Halide
Mapper
Place and Route
Configured CGRA
CoreIR Graph
Configuration Bitstream

## Slide 3: Challenges with Jade CGRA
1. PE supports only simple integer operations
  Porting applications that use floating point requires application expertise and manual effort

## Slide 4: Challenges with Jade CGRA
Memory supports only line buffered pipelines
  Most new applications even for imaging and vision use neural networks
  Need a memory hierarchy with double buffers for energy-efficiency
3 3 convolution
Multi-channel 3 3 convolution
Input
K of these
Line Buffer
Double Buffer

## Slide 5: Challenges with Jade CGRA
Multi-channel 3 3 convolution
K of these
1. Bring in tiles of inputs and weights into local memory reuse them as much as you can
2. Use a double buffer to overlap compute on current tile and fetching of next tile
3. Use a hierarchy of double buffers to maximize energy-efficiency
Memory supports only line buffered pipelines
  Most new applications even for imaging and vision use neural networks
  Need a memory hierarchy with double buffers for energy-efficiency
Image from: Jeff Setter

## Slide 6: Challenges with Jade CGRA
Configuration over JTAG is slow
  Large applications with multiple kernels don’t fit on the CGRA – need fast reconfiguration

## Slide 7: Key (application driven!) architectural changes in Garnet CGRA
Floating point support, and executing complex operations like divide using multiple PEs
Addition of a global buffer to create a memory hierarchy for efficiently executing neural networks, and double buffer support in all memories
Fast reconfiguration support using global buffer and control processor
Addition of configurable power domains

## Slide 8: Tomorrow’s talks
How did we update our design methodology to
  Incorporate architectural changes easily
  While maintaining an end-to-end application flow

## Slide 9: Magma and CoreIR Leonard Truong
Magma is our hardware description language embedded in Python
A magma circuit is basically a bunch of functional units wired together == Verilog module
Makes it possible to create higher-level domain-specific languages (DSLs)
  For processors (peak), finite state machines (silica), verification (fault) etc.
Python
Magma
Python meta-programs magma
Much more powerful than SystemVerilog’s parameter and generate and Genesis’s text-based templating!
Image from: Lenny Truong

## Slide 10: Magma Circuit
import magma as m
import mantle
from full_adder import FullAdder_
def DefineAdd(n):
class Adder_(m.Circuit):
name = f”Add{n}”
IO = [
“I0”, m.In(m.UInt(n)),
“I1”, m.In(m.UInt(n)),
“CIN”, m.In(m.Bit),
“O”, m.Out(m.UInt(n)),
“COUT”, m.Out(m.Bit),
]
@classmethod
def definition(io):
O = []
COUT = io.CIN
for i in range(n):
fulladder = FullAdder_()
OI, COUT = fulladder(io.I0[i], io.I1[i], COUT)
O.append(OI)
io.O <= m.uint(OI)
io.COUT <= COUT
return Adder_
Python Generator

## Slide 11: Magma and CoreIR
Magma compiles into CoreIR – which is our LLVM-style hardware intermediate representation and compiler infrastructure
CoreIR
FPGA
CGRA
ASIC
“LLVM for HW”
Verilog
Magma
Chisel
Halide
…

## Slide 12: CoreIR Primitives
Bitwise | buf, not, and, or, xor, andr, orr, xorr, shl, lshr, ashr
Arithmetic | neg, add, sub, mul, udiv, urem, sdiv, srem, smod
Comp | eq, neq, slt, sgt, sle, sge, ult, ugt, ule, uge
Stateful | reg, regrst, mem
Other | mux, slice, concat, zext, sext
Magma circuit == Verilog module == CoreIR graph of these primitives

## Slide 13: CoreIR Passes
Constant folding
Dead circuit elimination
Elaboration of generators
Verification (for example map to SMT)
Technology mapping
Linking
Notes: Debugging support (create name table)

## Slide 14
CoreIR
Magma
Higher Level DSLs
Image source: https://physicsforme.com/2011/07/19/best-ever-measurement-of-earths-radioactivity/

## Slide 15
Image source: Jesse Varner - Raft Lake and the Little Wind River Valley beyond, https://www.flickr.com/photos/molas/1364382020/in/photostream/
Peak
PE DSL
Lake
Memory DSL
Canal
Interconnect DSL

## Slide 16: Lassen and Peak Ross Daly
Diablo
Lassen
Whitney
Tapeout
Apr 2018
Jun 2019
…
Image source: https://pngio.com/images/png-77798.html

## Slide 17: Diablo
data0
Two 16 bit operands
Three 1 bit operands
8 entry
1 bit lut register
res
ALU
Add
Mult
And
…
res_p
data1
bit0
bit1
bit2
en_acc
Flag Logic

## Slide 18: Lassen
We wanted several new architectural features in Lassen
  Native floating point add and multiply
  Floating point micro-ops to easily implement complex operations (like divide, exp etc.) using multiple PEs and memory
  Multi-precision integer ops
Without breaking the application flow!

## Slide 19: Peak: PE DSL
Python-embedded DSL for describing the ISA and functional model of a PE
Has precise formal semantics
Automatically derive
  RTL (using Magma/CoreIR)
  Rewrite rules (from CoreIR primitive to PE instruction) for the mapper (using SMT)
    Generate SMT formula for CoreIR primitive and PE (given an instruction). Use SMT solver to prove the two formulas are the same.
  Collateral for bitstream generation

## Slide 20: Peak

## Slide 21: Memory and Lake Taeyoung Kong, Qiaoyi Liu
SRAM 0
SRAM 1
Two single port memory banks
FIFO Ctrl
Line Buffer Ctrl
SRAM
SRAM 0
SRAM 1
Two single port memory banks
FIFO Ctrl
General Line Buffer Ctrl
Double Buffer Ctrl
SRAM
Modes
Modes
SRAM 0
SRAM 1
Two single port memory banks
Unified Buffer with Address Generators
SRAM
Modes

## Slide 22: Global Buffer
 | 29 | 30 | 31
0 | 1 | 2 | 3 | 4 | 
Highly banked global buffer provides configurable capacity and bandwidth for data and bitstream
…
64b
0
1
2
3
4
28
29
30
31
…
Programmable Interconnect for Data and Configuration
Distributed Address Generators
Fast parallel reconfiguration

## Slide 23: Global Buffer
 | 29 | 30 | 31
0 | 1 | 2 | 3 | 4 | 
Highly banked global buffer provides configurable capacity and bandwidth for data and bitstream
…
64b
0
1
2
3
4
28
29
30
31
…
Programmable Interconnect for Data and Configuration
Distributed Address Generators
Fast parallel reconfiguration
Inputs
Weights
Config
Psums

## Slide 24: Interconnect and Canal Keyi Zhang
PE
CB
Connection box (CB)
10 vertical and horizontal 16 bit tracks
5 driven up/left, 5 driven down/right
10-to-1 mux
A
B
Similar 1 bit CBs for 1 bit inputs from 10 horizontal and vertical 1 bit tracks
CB
SB

## Slide 25: Switch Box
SB
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
Pipeline register
PE

## Slide 26: Interconnect and Canal
Place and route tool routes the output from one tile to the input of another tile by configuring these muxes
Image from: Keyi Zhang

## Slide 27: CB design choices
CB Bias - which track direction and track number the CB is connected to
CB
CB
PE
2 20-to-1 muxes
B (identical mux as A)
SB
A
In Garnet we changed the bias

## Slide 28: SB design choices
Number of tracks
The length of each track segment
Internal SB topology
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
PE
1

## Slide 29: Canal
Canal lets you
  Easily experiment with these interconnect design choices
  Snap in arbitrary cores – inspects the interfaces to determine how many and what type of CBs and SBs the core needs
  Generates the routing graph which feeds into the place and route tool
  Generates configuration bitstream

## Slide 30: Garnet and Gemstone Raj Setaluri, Alex Carsello
What is Gemstone?
  Library of reusable CGRA components written in Magma/higher level DSLs
    PE, Memory, Interconnect etc.
  Methods that enable you to write passes on the RTL and a library of reusable passes
What is Garnet?
  Our second generation CGRA built using gemstone components and passes
Image source: https://www.nwgems.com/products/natural-fine-intense-deep-red-garnet-oval-tanzania-top-grade

## Slide 31: Gemstone Pass Example
Global Controller
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
…
…
Global Controller
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
…
…
Pass
River Routing of Global Signals

## Slide 32: Gemstone Passes
Hardware design process should capture more than just the RTL
  Logical Design (RTL), Physical Design, Testing/Verification, Software/API
Gemstone enables staged hardware generation
  Each pass encapsulates different design knowledge
  Passes can transform RTL to make it amenable to other portions of the design flow
  Passes can generate collateral for other portions of the design flow (like physical design, verification)

## Slide 33: Gemstone Passes
Logical Description
Logical Description’
Logical Description’’
Logical Description’’’
Place and Route Flow
RTL with power domains
RTL with configuration registers distributed
Initial RTL from logical designer
Pass
RTL with global signals river routed
Pass
Pass
Verilog to physical design
Floorplan
Testing Collateral

## Slide 34: SoC Rick Bahr, Gedeon Nyengele, Teguh Hofstee
CGRA
Global Buffer
DMA Engine
DMA Engine
TLX
CoreLink
Control Processor
(ARM Cortex M3)
Nested Vector Interrupt Controller (NVIC)
Wake-up Interrupt Controller (WIC)
Memory Protection Unit (MPU)
I-Bus
D-Bus
Debug JTAG
TLX
DRAM
DRAM Controller
Application Processor
FPGA
SRAM
AXI
AXI
AXI
AXI
AXI
AHB
AHB
SRAM
AXI
SoC

## Slide 35: Visual Applications and Halide-to-Hardware Jeff Setter, Xuan Yang
CGRA Programming Toolchain
Halide Compiler
Application in Halide
Mapper
Place and Route
Configured CGRA
CoreIR Graph
Configuration Bitstream

## Slide 36: Visual Applications and Halide-to-Hardware Jeff Setter, Xuan Yang
Inferring computation is easy, hard part is inferring the memories and their access patterns
Our key realization was that these seemingly different access patterns can be expressed using a unified buffer template
Application in Halide
HalideIR
Extract Logical Unified Buffer Parameter
Map to (Many) Physical Unified Buffers

## Slide 37: Tomorrow’s Program
9:00 | Overview of the Chip | Priyanka Raina
9:15 | Magma and CoreIR | Leonard Truong
9:40 | Lassen and Peak | Ross Daly
10:05 | Memory and Lake | Taeyoung Kong, Qiaoyi Liu
10:30 | Break | 
11:00 | Interconnect and Canal | Keyi Zhang
11:25 | Garnet and Gemstone | Raj Setaluri, Alex Carsello
11:50 | SOC | Rick Bahr, Gedeon Nyengele, Teguh Hofstee
12:15 | Lunch | 
1:30 | A Semiconductor Industry Perspective | Nafea Bshara
2:10 | Visual Applications and Halide to Hardware | Jeff Setter, Xuan Yang
2:35 | Company Interactions | Pat Hanrahan
3:00 | Break | 
3:30 | Break into groups for feedback | 
4:30 | Feedback report out |